## Slide 1: Hardware Acceleration for Cluster Fault Tolerance in Hybrid CMOS/non-CMOS Memories
Dissertation Defence Yuqi Guo

## Slide 2: 1. Motivation and Problem
Why this project matters
Hybrid CMOS/non-CMOS memories offer high density and low cost, but they are vulnerable to spatially correlated cluster faults.
Traditional ECC schemes are often evaluated for independent random errors, not realistic burst faults.
Previous studies mainly relied on simulation; hardware-validated comparison was still missing.
Core research question
Which ECC design gives the best trade-off between fault tolerance, latency, area, power, and storage efficiency on real FPGA hardware?

## Slide 3: 2. Project Goal and Objectives
Project goal
To design and implement an FPGA-based hardware acceleration platform for fair benchmarking of multiple ECC algorithms under realistic cluster-fault conditions.
Objectives
Implement and compare 6 configurations:
  2NRM-RRNS Parallel
  2NRM-RRNS Serial
  3NRM-RRNS
  C-RRNS-MLD
  C-RRNS-MRC
  RS(12,4)
Evaluate four key dimensions:
  fault tolerance
  decoding latency
  FPGA resource and power cost
  storage efficiency # 3. Methodology and Experimental Setup
Evaluation flow
Phase 1: MATLAB simulation for theoretical baseline.
Phase 2: FPGA implementation for hardware validation.
Same encode-inject-decode-compare loop is used for every configuration.
Test settings
Device: Artix-7 xc7a100t (Arty A7-100T)
Clock: 50 MHz
Fault modes:
  random single-bit injection
  cluster burst injection with burst length 1-15

## Slide 4: 4. FPGA Platform Architecture

## Slide 5
Key idea
The PC controls configuration and visualisation, while the FPGA autonomously performs the full BER sweep and uploads consolidated results through UART.

## Slide 6: 5. Main Innovation: Probabilistic Fault Injection Engine
Key features
Uses a 32-bit Galois LFSR as the pseudo-random source.
Supports both random single-bit and cluster burst injection.
BER is controlled by threshold comparison instead of a fixed schedule.
Boundary-safe burst masks are precomputed offline and stored in ROM.
Why it matters
This makes the platform resource-efficient, reproducible, and reusable for benchmarking different ECC algorithms.

## Slide 7: 6. Why the Test Platform Is Strong
Advantages of the proposed FPGA test platform
Fair comparison: all algorithms share the same test infrastructure and clock condition.
Hardware validated: results are measured on a Xilinx Artix-7 FPGA, not simulation alone.
Low overhead fault injection: the probabilistic injector uses only two BRAMs.
Scalable experiments: supports 101 BER points from 0% to 10% and 100,000 samples per point.
Extensible architecture: new ECCs can be added with the wrapper interface.
Cross-validated: FPGA curves closely match MATLAB results, increasing credibility.

## Slide 8: 7. Random Single-Bit Results

## Slide 9
Main observation
FPGA and MATLAB curves show close agreement.
Correcting ECCs remain strong at low BER, while C-RRNS-MRC drops fastest.

## Slide 10: 8. Cluster Burst Results at Representative Length L=12

## Slide 11
Main observation
C-RRNS-MLD and RS(12,4) show the strongest burst resilience.
Burst-fault ranking differs from random-bit testing, showing why a realistic fault model is necessary.

## Slide 12: 9. Quantitative Comparison of Key Results
Algo | Burst | Dec. cycles | Efficiency
C-RRNS-MLD | 14 | 928 | 26.2%
RS(12,4) | 13 | 127 | 33.3%
3NRM-RRNS | 11 | 2048 | 33.3%
2NRM-P | 8 | 24 | 39.0%
2NRM-S | 7 | 1047 | 39.0%

## Slide 13
Takeaway
Most reliable: C-RRNS-MLD
Fastest: 2NRM-P
Most compact: 2NRM

## Slide 14: 10. Latency Comparison

## Slide 15
Conclusion from latency results
The 2NRM-RRNS Parallel decoder is the fastest correcting design.
The parallel implementation achieves a major acceleration over the serial version.
The result clearly exposes the resource-latency trade-off of parallel MLD.

## Slide 16: 11. Resource and Storage Comparison

## Slide 17
Key message
2NRM-Parallel achieves high speed at the highest LUT/FF and power cost.
2NRM is the most storage-efficient option, while C-RRNS-MLD gives the strongest protection.

## Slide 18: 12. Main Conclusions
Major conclusions from the dissertation
The project successfully delivers a working FPGA benchmarking platform for ECC evaluation under cluster faults.
C-RRNS-MLD shows the strongest burst-fault tolerance in the explored design space.
2NRM-RRNS Parallel offers the lowest decode latency, but its area and power cost are high.
2NRM-RRNS provides the best storage efficiency for overhead-sensitive systems.
The close agreement between FPGA and MATLAB results confirms the correctness and reliability of the evaluation method.

## Slide 19: 13. Contributions and Future Work
Contributions
A reusable FPGA evaluation platform with unified wrappers.
A low-resource probabilistic fault injection engine.
The first hardware-level quantification of the parallel vs serial 2NRM-RRNS trade-off.
Future work
evaluate wider data words and more ECC variants
reduce LFSR correlation with stronger random sources
migrate the framework toward ASIC or real hybrid memory devices

## Slide 20: Appendix A. Fault Injection Algorithm
Probabilistic injection procedure
Generate encoded codeword.
Lock one random seed for the full BER sweep.
For each BER point, compute the injection threshold.
Use the 32-bit Galois LFSR to decide whether to inject an error.
If random mode is selected, test valid bits independently.
If burst mode is selected, apply one ROM-based contiguous burst mask.
Decode and compare with the original data to record pass or fail.
Purpose
This appendix shows that the fault injector is not a simple random flip unit, but a controlled and reproducible hardware evaluation algorithm.

## Slide 21: Appendix B. Backup Figure: Burst-Length Impact

## Slide 22
Backup message
These curves support the final claim that C-RRNS-MLD provides the best extreme cluster-fault tolerance, with RS as the strongest balanced alternative.

## Slide 23: Thank You
Questions?
Thank you for listening.